## Slide 1: KCEC Network Redundancy

## Slide 2: Core Router Redundancy
2 Core Routers – Juniper MX240
  Redundant Power
  Redundant Control Board
  Juniper Core Routers can be connected to provide Inter-Chassis Redundancy aka Virtual Chassis.

## Slide 3: MX240
4 Slot Chassis
Physical size
  Height: 5RU, Depth: <800mm deep
System capacity
  4 slots – 2 available for Fabric Cards / REs
  Up to 960Gbps (full-duplex) from 3 line cards today
    NG Fabric supports 1.6Tbps per chassis
  System reuses existing SCBs, REs, DPCs and MPCs – common across all MX platforms
Dependable hardware
  Passive Mid-Plane
  Redundant Routing Engines (1+1)
  Redundant Switching Fabric (1+1)
  Distributed Packet Forwarding Architecture
  Redundant Power
Power and cooling
  Side to Side cooling
  Holds up to 4 power supplies (1+1 DC, 1+1 AC 200-240VAC, 2+2 AC 100-110VAC)
  Rear-side power cabling
MX240

## Slide 4: MX Virtual Chassis:
Single Cluster Control Plane
Active State Mirror
Distributed Redundancy
Scalable Bandwidth
Services at Scale
GRES/NSR SYNCHRONIZATION
2 Core Routers – Juniper MX240
  Each Router has Redundant Power Supply
  Each Router has Redundant Control Board.
  Chassis are Redundant through Virtual Chassis.
Notes: Virtual Chassis technology allows up to eight interconnected physical chassis to be monitored and managed as a single logical device. Virtual Chassis offers the following benefits:
• Simplifies manageability by providing a unified control plane for all physical chassis
• Improves resource utilization by intelligently employing interfaces and service line cards on physically different chassis, providing customers with a “pay-as-you-grow” model.
• Protects user sessions across physical chassis, line card or port failure, using stateful redundancy so users are completely unaware of failures.
• Supports sophisticated resiliency techniques within the Virtual Chassis.

## Slide 5: Core Network Redundancy
KCEC Architecture is Ring-Based
Hub Site Switches are equipped with Redundant Power.
Provides redundant path to reach Core Routers.
  Fiber Cut will cause switches to converge to alternate Path.
Few Sites are in Hub-Spoke form.
  These site are prone to single point of failure, due to non-diverse fiber path.
  Switch/OLT failure can also contribute to single point of failure, however will not affect any other sites.

## Slide 6: Core Network

## Slide 7: ISP Redundancy Options (Multi-homing)
KCEC GPON
Option 1 : Single Site, Dual Router to Single ISP
ISP -1
Primary
Secondary
HE-R1
HE-R2
HE-R1
HE-R2

## Slide 8: ISP Redundancy Options (Multi-homing)
Option 2 : Single Site, Dual Router to Two ISPs
KCEC GPON
HE-R1
HE-R2
ISP -1
Primary
Secondary
ISP -2

## Slide 9: ISP Redundancy Options (Multi-homing)
KCEC GPON
Option 3 : Single Site, Single Virtual Chassis Router to Two ISPs
ISP -1
Primary
Secondary
ISP -2
2 Routers connected in Virtual Chassis Mode to act as Single Router

## Slide 10: Multi-Homing
Effective Mutli-Homing of Network is dependent on
  Number of Uplinks
  Number of ISP
  Number of Routers
  Tuning of BGP Protocol
  Identification of Primary and Standby Link.
  Uplinks can also load balance traffic with proper tuning of Router configurations.
  ISP polices.